Stormwater Pollution Prevention Plan

for:

The Chalets at Ski Lake Phase 5

Highway 39 & Snowbasin Road

Huntsville, Utah  84317

Operator & SWPPP Contact:

Valley Enterprise Investment Company, LLC.

Ray Bowden - President

5393 East 6850 North

Eden, UT. 84310

801-725-1517

SWPPP Preparation Date:

November 22, 2011

Estimated Project Dates (TBD by Owner):

Project Start Date:  __ __ / __ __ / __ __ __ __

Project Completion Date: __ __ / __ __ / __ __ __ __

Contents

SECTION 1: SITE EVALUATION, ASSESSMENT, AND PLANNING	1

1.1	Project/Site Information	1

1.2	Contact Information/Responsible Parties	1

1.3	Nature and Sequence of Construction Activity	2

1.4	Soils, Slopes, Vegetation, and Current Drainage Patterns	3

1.5	Construction Site Estimates	3

1.6	Receiving Waters	3

1.7	Site Features and Sensitive Areas to be Protected	3

1.8	Potential Sources of Pollution	4

1.9	Endangered Species Certification	4

1.10	Historic Preservation	4

1.11	Applicable Federal, Tribal, State or Local Programs	4

1.12	Maps	4

SECTION 2: EROSION AND SEDIMENT CONTROL BMPS	5

2.1	Minimize Disturbed Area and Protect Natural Features and Soil	5

2.2	Phase Construction Activity	5

2.3	Control Stormwater Flowing onto and through the Project	6

2.4	Stabilize Soils	6

2.5	Protect Slopes	6

2.6	Protect Storm Drain Inlets	7

2.7	Establish Perimeter Controls and Sediment Barriers	7

2.8	Retain Sediment On-Site	7

2.9	Establish Stabilized Construction Exits	8

2.10	Additional BMP’s	8

SECTION 3: GOOD HOUSEKEEPING BMPS	9

3.1	Material Handling and Waste Management	9

3.2	Establish Proper Building Material Staging Areas	9

3.3	Designate Washout Areas	9

3.4	Establish Proper Equipment/Vehicle Fueling and Maintenance Practices	10

3.5	Control Equipment/Vehicle Washing	10

3.6	Spill Prevention and Control Plan	11

3.7	Any Additional BMPs	14

3.8	Allowable Non-Stormwater Discharge Management	14

SECTION 4: SELECTING POST-CONSTRUCTION BMPs	15

SECTION 5: INSPECTIONS	16

5.1	Inspections	16

5.2	Delegation of Authority	16

5.3	Corrective Action Log	16

6.1	Recordkeeping	17

6.2	Log of Changes to the SWPPP	17

6.3	Training	17

SECTION 7: FINAL STABILIZATION	18

SECTION 8: CERTIFICATION AND NOTIFICATION	19

SWPPP APPENDICES	20

Appendix A – General Location Map

Appendix B – Site Maps

Appendix C – Construction General Permit

Appendix D – NOI and Acknowledgement Letter from EPA/State

Appendix E – Inspection Reports

Appendix F – Corrective Action Log

Appendix G – SWPPP Amendment Log

Appendix H – Subcontractor Certifications/Agreements

Appendix I – Grading and Stabilization Activities Log

Appendix J – Training Log

Appendix K – Delegation of Authority

Appendix L – Standards and Specifications For Selected BMP’s

Appendix M – Additional Non-Selected BMP’s

# SECTION 1: SITE EVALUATION, ASSESSMENT, AND PLANNING

## 1.1	Project/Site Information

| Project/Site Name: The Chalets at Ski Lake Phase 5 |
| --- |
| Project Street/Location: Highway 39 & Snowbasin Road |
| City: Huntsville | State: Utah | ZIP Code: 84317 |
| County or Similar Subdivision: Weber County |
| Latitude/Longitude (Use one of three possible formats, and specify method) |
| Latitude: | Longitude: |
| 41º 14' 57'' N | -111º 47' 51'' W |
| Method for determining latitude/longitude: |
| USGS topographic map (specify scale: ) | EPA Web site | GPS |
| Other (please specify): Google Earth |
| Is the project located in Indian country? Yes No |
| If yes, name of Reservation, or if not part of a Reservation, indicate "not applicable." |
| Is this project considered a federal facility? Yes No |
| NPDES project or permit tracking number*: |
| *(This is the unique identifying number assigned to your project by your permitting authority after you have applied for coverage under the appropriate National Pollutant Discharge Elimination System (NPDES) construction general permit.) |

## 1.2	Contact Information/Responsible Parties

Owner:

Valley Enterprise Investment Company, LLC.

Ray Bowden - President

5393 East 6850 North

Project Manager or Site Supervisor (TBD):

Company:

Name:

Address:

City, State, Zip Code:

Telephone Number:

Fax/Email:

SWPPP Contact (TBD):

Company:

Name:

Address:

City, State, Zip Code:

Telephone Number:

Fax/Email:

This SWPPP was Prepared by:

Great Basin Engineering

Heather Avner

5746 South 1475 East, Suite #200

Ogden, Utah 84403

Phone: (801) 394-4515

Fax: (801) 392-7544

Subcontractor(s) (TBD):

Company:

Name:

Address:

City, State, Zip Code:

Telephone Number:

Fax/Email:

Emergency 24-Hour Contact (TBD):

Company:

Name:

Telephone Number:

## 1.3	Nature and Sequence of Construction Activity

This project is the 5th phase of construction of the Ski Lake Chalet project in Ogden Valley, Utah. The project consists of constructing a road with residential lots.

What is the function of the construction activity?

Residential Commercial Industrial Road Construction Linear Utility

Other (please specify):

Estimated Project Start Date (TBD by Owner): __ __ / __ __ / __ __ __ __

Estimated Project Completion Date (TBD by Owner): __ __ / __ __ / __ __ __ __

## 1.4	Soils, Slopes, Vegetation, and Current Drainage Patterns

The soil in the area is an impermeable clayey soil. The site is located on a mountain side. After construction of the road the slope of the land will be similar to the existing slope of the mountain. A minimal amount of water flows onto the site. A public storm drain system collects all the water via pipe which continues east to a detention pond located in the chalets at Ski Lake phase 1. Upon completion of the project, new storm drain boxes will be installed in the gutter of the road and the site will drain through the boxes. The existing vegetation on site consists of sage brush, bushes and wild grasses.

## 1.5	Construction Site Estimates

| The following are estimates of the construction site. |
| --- |
| Total project area: | 7.45 acres |
| Construction site area to be disturbed : | 1.98 acres |
| Percentage impervious area before construction: | 0% |
| Runoff coefficient before construction: | 0.15 |
| Percentage impervious area after construction: | 33% |
| Runoff coefficient after construction | 0.40 |

## 1.6	Receiving Waters

The water on the site will flow to proposed storm drain inlet boxes where it is then carried through pipes to a detention pond located off site. From the detention pond, the water will then flow via Smith Creek to Pine View Reservoir.

## 1.7	Site Features and Sensitive Areas to be Protected

Not Applicable

## 1.8	Potential Sources of Pollution

The construction of the road on the site may affect the quality of the stormwater discharge from the site. Because the site is located on a mountain side, erosion is potential source pollution.

## 1.9	Endangered Species Certification

Not Applicable

## 1.10	Historic Preservation

Not Applicable

## 1.11	Applicable Federal, Tribal, State or Local Programs

Not Applicable

## 1.12	Maps

See Appendix B:

Sheet 1 – Existing Site Conditions

Sheet 2 – Proposed Site Conditions w/BMP’s Shown

# SECTION 2: EROSION AND SEDIMENT CONTROL BMPS

BMP’s to be used are shown on drawing Sheet 2 – Proposed Site Conditions w/BMP’s.

## 2.1	Minimize Disturbed Area and Protect Natural Features and Soil

The SWPP areas of disturbance are shown on drawing Sheet 2.  Also shown on Sheet 2 are the BMP’s that will be used to limit disturbance outside of the project site.  A silt fence will be installed to prevent sediment from flowing off the site.  Erosions blankets will be included to minimize erosion.  Inlet protection will also be utilized around the proposed inlet boxes.

## 2.2	Phase Construction Activity

The phases indicated below are for BMP construction sequencing for the Chalets at Ski Lake Phase 5.

- Phase I

- Clear & Grub Existing Vegetation Phase

- BMP’s to be used during Phase I

  - Silt Fence

  - Equipment Repair & Maintenance

  - Construction Entrance

- Phase II

- Utility Construction Phase

- BMP’s to be used during Phase II

  - Silt Fence

  - Inlet Protection

    - Silt Snake

  - Concrete Waste Management

  - Equipment Repair & Maintenance

  - Surface Roughening

  - Mulching

  - Construction Entrance

- Phase III

- Finish Grading Phase

- BMP’s to be used during Phase II

  - Silt Fence

  - Inlet Protection

    - Silt Snake

  - Concrete Waste Management

  - Erosion Control

  - Equipment Repair & Maintenance

  - Surface Roughening

  - Mulching

  - Temporary and Permanent Seeding

  - Construction Entrance

## 2.3	Control Stormwater Flowing onto and through the Project

Not Applicable

## Stabilize Soils

| BMP Description: Surface Roughening |
| --- |
| Recommended Maintenance: | If erosion in the form of rills (small waterways formed by runoff) is evident, perform machine roughening of area. For vegetated slopes reseed areas that are bare or have been reworked. |
| Schedule for Maintenance and Inspection: | Weekly and after any storm event. |
| Responsible Staff: | Contractor |

| BMP Description: Temporary and Permanent Seeding |
| --- |
| Recommended Maintenance: | Provide irrigation as required to establish growth and to maintain plant cover through duration of project. Reseed as necessary to provide 75% coverage. Remediate any areas damaged by erosion or traffic. When 75% coverage is achieved inspect monthly for damage and remediate as necessary. |
| Schedule for Maintenance and Inspection: | Monthly and after rainfall. |
| Responsible Staff: | Contractor |

| BMP Description: Mulching |
| --- |
| Recommended Maintenance: | Inspect mulched areas after every rainfall event and at a minimum of monthly. Replace mulch on any bare areas and reanchor as necessary. Clean and replace downgradient controls as necessary. |
| Schedule for Maintenance and Inspection: | Monthly and after every rainfall event. |
| Responsible Staff: | Contractor |

## 2.5	Protect Slopes

| BMP Description: Erosion Control |
| --- |
| Permanent Temporary |
| Recommended Maintenance: | Check for erosion and undermining periodically, particularly after rainstorms. Repair dislocations or failures immediately. Monitor erosion control until slope is completely stabilized. |
| Schedule for Maintenance and Inspection: | See attached Erosion and Sediment Control Inspection Form. |
| Responsible Staff: | Contractor |

## 2.6	Protect Storm Drain Inlets

| BMP Description: Inlet Protection |
| --- |
| Recommended Maintenance: | Replace clogged filter fabric. Clean sediment from stone filters. Do not wash collected sediments into storm drains – remove to soil stockpile. |
| Schedule for Maintenance and Inspection: | Weekly and following storms and Daily during prolonged rainy periods |
| Responsible Staff: | Contractor |

## 2.7	Establish Perimeter Controls and Sediment Barriers

| BMP Description: Silt Fence |
| --- |
| Recommended Maintenance: | Repair damaged fencing immediately. Intercept concentrated flows and reroute. Remove sediment accumulations at 6-inches. Replace deteriorated fencing material. Properly dispose of used fencing. |
| Recommended Schedule of Maintenance and Inspection: | Weekly and following Storms. |
| Responsible Staff: | Contractor |

## 2.8	Retain Sediment On-Site

Not Applicable

## 2.9	Establish Stabilized Construction Exits

| BMP Description: Construction Entrance |
| --- |
| Recommended Maintenance: | Quarry spalls (or hog fuel) shall be added if the pad is no longer in accordance with the specifications. If the rock (or hog fuel) entrance is not working to keep streets clean, then install wheel wash, sweep streets, or wash streets if wash water can be collected. |
| Recommended Schedule of Maintenance and Inspection: | Daily |
| Responsible Staff: | Contractor |

| BMP Description: Construction Road Stabilization |
| --- |
| Recommended Maintenance: | Inspect stabilized areas regularly, especially after large storm events. Add rock (hog fuel), gravel, etc. as needed to maintain a stable surface which won’t erode. |
| Recommended Schedule of Maintenance and Inspection: | Daily |
| Responsible Staff: | Contractor |

## 2.10	Additional BMP’s

Not Applicable

# SECTION 3: GOOD HOUSEKEEPING BMPS

## 3.1	Material Handling and Waste Management

- All pollutants, including waste materials and demolition debris, that occur on-site during construction will be handled in a way that does not contaminate storm water.

- All chemicals including liquid products, petroleum products, water treatment chemicals, and wastes stored on site will be covered and contained and protected from vandalism.

- Maintenance and repair of all equipment and vehicles involving oil changes, hydraulic system drain down, de-greasing operations, fuel tank drain down and removal, and other activities which may result in the accidental release of contaminants, will be conducted under cover during wet weather and on an impervious surface to prevent the release of contaminants onto the ground.  Materials spilled during maintenance operations will be cleaned up immediately and properly disposed of.

- Wheel wash water will be settled and discharged on site by infiltration.  Wheel wash water will not be discharged to the storm water system or the storm water treatment system.

- Application of agricultural chemicals, including fertilizers and pesticides, will be conducted in a manner and at application rates that will not result in loss of chemical to storm water runoff. Manufacturers’ recommendations will be followed for application rates and procedures.

- pH-modifying sources will be managed to prevent contamination of runoff and storm water collected on site.  The most common sources of pH-modifying materials are bulk cement, cement kiln dust (CKD), fly ash, new concrete washing and curing waters, waste streams generated from concrete grinding and sawing, exposed aggregate processes, and concrete pumping and mixer washout waters.

## 3.2	Establish Proper Building Material Staging Areas

Not Applicable

## 3.3	Designate Washout Areas

| BMP Description: Concrete Waste Management |
| --- |
| Recommended Maintenance: | Inspect subcontractors to ensure that concrete wastes are being properly managed. If using a temporary pit, dispose of hardened concrete on a regular basis. |
| Recommended Schedule of Maintenance and Inspection: | As needed |
| Responsible Staff: | Contractor |

## 3.4	Establish Proper Equipment/Vehicle Fueling and Maintenance Practices

| BMP Description: Equipment Repair & Maintenance |
| --- |
| Recommended Maintenance: | Inspect equipment frequently for leaks and repairs. Maintain in contractor designated areas only. Legally dispose of used oils, fluids, and lubricants. |
| Recommended Schedule of Maintenance and Inspection: | As needed |
| Responsible Staff: | Contractor |

## 3.5	Control Equipment/Vehicle Washing

| BMP Description: Equipment & Vehicle Wash Down Area – A stabilized pad of crushed stone for general washing of equipment and construction vehicles. |
| --- |
| Installation Schedule: | Clear & grub area and grade to provide maximum slope of 1%. Compact subgrade and place filter fabric if desired. Place coarse aggregate, 1 to 2 ½” in size, to a minimum depth of 8”. Install silt fence down gradient. |
| Maintenance and Inspection: | Inspect daily for loss of gravel or sediment buildup. Inspect adjacent area for sediment deposit and install additional controls as necessary. Repair area and replace gravel as required to maintain control in good working condition. Expand stabilized area as required to accommodate activities. Maintain silt fence. |
| Responsible Staff: | Contractor |

## 3.6	Spill Prevention and Control Plan

- The site superintendent will be notified immediately when a spill, or the threat of a spill, is observed.  The superintendent will assess the situation and determine the appropriate response.

- If spills represent an imminent threat of escaping ESC facilities and entering the receiving waters, facility personnel will respond immediately to contain the release and notify the superintendent after the situation has been stabilized.

- Spill kits containing materials and equipment for spill response and cleanup will be maintained at the site.  Each spill kit may contain:

- Oil absorbent pads (one bale)

- Oil absorbent booms (40 feet)

- 55-gallon drums (2)

- 9-mil plastic bags (10)

- Personal protective equipment including gloves and goggles

- If an oil sheen is observed on surface water (e.g., settling ponds, detention pond, swales), absorbent pads and/or booms will be applied to contain and remove the oil.  The source of the oil sheen will also be identified and removed or repaired as necessary to prevent further releases.

- The site superintendent, or his designee, will be responsible for completing the spill reporting form and for reporting the spill to the appropriate state or local agency (see Forms at the end of this section).

- Facility personnel with primary responsibility for spill response and cleanup will receive training from the site superintendent.  This training will include identifying the location of spill kits and other spill response equipment and the use of spill response materials.

- Spill response equipment will be inspected and maintained as necessary to replace any materials used in spill response activities.

- Any spill of oil which 1) violates water quality standards, 2) produces a “sheen” on a surface water, or 3) causes a sludge or emulsion must be reported immediately by telephone to the National Response Center Hotline at (800) 424-8802.

- Any oil, hazardous substance, or hazardous waste release which exceeds the reportable quantity must be reported immediately by telephone to the National Response Center Hotline at (800) 424-8802.

- Any spill of oil or hazardous substance to waters of the state must be reported immediately by telephone to the State of Utah Department of Environmental Quality, Rand Fisher at (801) 533-6065.

- Any release of a hazardous substance that may be a threat to human health or the environment must be reported to the State of Utah Department of Environmental Quality, Rand Fisher at (801) 533-6065.

Emergency Phone Numbers

| Fire, Police, Ambulance |  | 911 |
| --- | --- | --- |
| Owner: |  |  |
| General Contractor | Office: Site |  |
|  | Mobile # |  |
| Subcontractors |  |  |
| Sub #1) | Office: |  |
| Sub #2 |  |  |
| Sub #3 |  |  |
| Sub #4 |  |  |
| City or County Contact |  |  |
| State Ecology Dept. |  |  |

Spill Report Form

| Location: |
| --- |
|  |  | Date:___________________ Time: |
| Regulatory agencies notified (date, time, person, agency, and how): |
| Material spilled: |
| Quantity spilled: |
| Source: Cause: |
| Extent of injuries (if any): Adverse environmental impact (if any): Immediate remedial actions taken at time of spill: Measures taken or planned to prevent recurrence: Additional comments: This report prepared by: (Signature) (Date) (Job title) |

## 3.7	Any Additional BMPs

Not Applicable

## 3.8	Allowable Non-Stormwater Discharge Management

Not Applicable

# SECTION 4: SELECTING POST-CONSTRUCTION BMPs

Not Applicable

# SECTION 5: INSPECTIONS

## 5.1	Inspections

1. Inspection Personnel: To be selected by Contractor

2. Inspection Schedule and Procedures: To be determined by Contractor See Appendix E – Inspection Reports

## 5.2	Delegation of Authority

See Appendix K – Delegation of Authority Duly Authorized Representative(s) for purposes of signing inspection reports, certifications, or other information (by Contractor if Applicable):

Company or Organization Name:

Name:

Position:

Address:

City, State, Zip Code:

Telephone Number:

Fax/Email:

## 5.3	Corrective Action Log

See Appendix F – Corrective Action Log

SECTION 6: RECORDKEEPING AND TRAINING

## 6.1	Recordkeeping

Records of the following will be retained for a minimum period of at least 3 years after the permit is terminated (see attached log):

Date(s) when major grading activities occur Date(s) when construction activities temporarily or permanently cease on a portion of the site Date(s) when an area is either temporarily or permanently stabilized

## 6.2	Log of Changes to the SWPPP

Changes to SWPPP documents and plans should be documented (see Appendix G – SWPPP Amendment Log).

## 6.3	Training

Contractor is responsible for:

- General stormwater and BMP awareness training for staff and subcontractors

- Detailed training for staff and subcontractors with specific stormwater responsibilities

See Appendix J – Training Log

# SECTION 7: FINAL STABILIZATION

- After construction has been completed, the site shall be swept clean, storm water inlets (grates and basins) shall be cleaned, and all waste and leftover materials shall be removed from the site.

- All landscaping and planting areas should be well maintained to prevent erosion.  Avoid over watering of landscaping.

- All paved areas should be swept weekly either by hand or by mechanical means to keep the site clear of dirt, dust, and debris.

- Waste materials on-site should be stored in covered containers which are cleaned out regularly.

- Testing of fire hydrants on-site shall not be conducted until the area where the water discharges has been swept clean of dirt and debris.

- Storm drain lines should be checked and cleaned annually to keep them clean and clear of debris.

- All on-site storm water inlets should be clearly marked “storm water only".

# SECTION 8: CERTIFICATION AND NOTIFICATION

I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gathered and evaluated the information submitted.  Based on my inquiry of the person or persons who manage the system, or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete.  I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations.

| Contractor Name: |  | Title: |  |
| --- | --- | --- | --- |
| Signature: |  | Date: |  |

# SWPPP APPENDICES

Appendix A – General Location Map

Appendix B – Site Maps

Appendix C – Construction General Permit

Appendix D – NOI and Acknowledgement Letter from State

Appendix E – Inspection Reports

Appendix F – Corrective Action Log

Appendix G – SWPPP Amendment Log

Appendix H – Subcontractor Certifications/Agreements

Appendix I – Grading and Stabilization Activities Log

Appendix J – Training Log

Appendix K – Delegation of Authority

Appendix L – Standards and Specifications For Selected BMP’s

Appendix M – Additional Non-Selected BMP’s

Appendix E – Inspection Reports

Erosion and Sediment Control Inspection Form

Inspector(s):________________________________Date:________________

Site Name and Location:___________________________________________

Current Weather Conditions:_____________	Last 24 Hours:______________

Erosion Prevention

| BMP Designation | O.K | Not O.K. | BMP Condition, Corrective Action, General Notes |
| --- | --- | --- | --- |
| Construction Access Trackout? Street Clean? |  |  |  |
| Soil Stabilization Signs of Erosion: Gullies? Slope Failures? Rills? |  |  |  |
| Slope Protection Plastic Condition? Grass Growing? Hydroseed Condition? Matting? |  |  |  |
| Perimeter Control Clearing Limits Marked? Silt Fences? Swales? |  |  |  |
| Conveyances Stable Ditches? Check Dams Intact? Sand Bags? Slope Drains? |  |  |  |
| TESC Management Revisions Required? |  |  |  |
| Water Management Infiltration System? Clean and Dirty Water Separated? Offsite Water Bypassing? |  |  |  |
| Outlet Protection Stabilized? |  |  |  |

Sediment Control

| BMP Designation | O.K | Not O.K. | BMP Condition, Corrective Action, General Notes |
| --- | --- | --- | --- |
| Storm water Detention And Monitoring |  |  |  |
| BMP Maintenance |  |  |  |
| Inlet Protection |  |  |  |
| Dust Control |  |  |  |
| Spill Prevention |  |  |  |
| Condition of Discharge Water |  |  |  |
| Comments:_______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________ |

Appendix F – Corrective Action Log

Project Name:

SWPPP Contact:

| Inspection Date | Inspector Name(s) | Description of BMP Deficiency | Corrective Action Needed (including planned date/responsible person) | Date Action Taken/Responsible person |
| --- | --- | --- | --- | --- |

Appendix G –SWPPP Amendment Log

Project Name:

SWPPP Contact:

| Amendment No. | Description of the Amendment | Date of Amendment | Amendment Prepared by [Name(s) and Title] |
| --- | --- | --- | --- |

Appendix H –Subcontractor Certifications/Agreements

SUBCONTRACTOR CERTIFICATION

STORMWATER POLLUTION PREVENTION PLAN

Project Number:

Project Title:

Operator(s):

As a subcontractor, you are required to comply with the Stormwater Pollution Prevention Plan (SWPPP) for any work that you perform on-site.  Any person or group who violates any condition of the SWPPP may be subject to substantial penalties or loss of contract.  You are encouraged to advise each of your employees working on this project of the requirements of the SWPPP.  A copy of the SWPPP is available for your review at the office trailer.

Each subcontractor engaged in activities at the construction site that could impact stormwater must be identified and sign the following certification statement:

I certify under the penalty of law that I have read and understand the terms and conditions of the SWPPP for the above designated project and agree to follow the BMPs and practices described in the SWPPP.

This certification is hereby signed in reference to the above named project:

Company:

Address:

Telephone Number:

Type of construction service to be provided:

Signature:

Title:

Date:

Appendix I –Grading and Stabilization Activities Log

Project Name:

SWPPP Contact:

| Date Grading Activity Initiated | Description of Grading Activity | Date Grading Activity Ceased (Indicate Temporary or Permanent) | Date When Stabilization Measures are Initiated | Description of Stabilization Measure and Location |
| --- | --- | --- | --- | --- |

Appendix J –SWPPP Training Log

Stormwater Pollution Prevention Training Log

Project Name:

Project Location:

Instructor’s Name(s):

Instructor’s Title(s):

Course Location: 	  Date:

Course Length (hours):

Stormwater Training Topic:  (check as appropriate)

| ( | Erosion Control BMPs | ( | Emergency Procedures |
| --- | --- | --- | --- |
| ( | Sediment Control BMPs | ( | Good Housekeeping BMPs |
| ( | Non-Stormwater BMPs |  |  |

Specific Training Objective:

Attendee Roster:  (attach additional pages as necessary)

| No. | Name of Attendee | Company |
| --- | --- | --- |
| 1 |  |  |
| 2 |  |  |
| 3 |  |  |
| 4 |  |  |
| 5 |  |  |
| 6 |  |  |
| 7 |  |  |
| 8 |  |  |
| 9 |  |  |
| 10 |  |  |

Appendix K –Delegation of Authority Form

Delegation of Authority

I, _______________________ (name), hereby designate the person or specifically described position below to be a duly authorized representative for the purpose of overseeing compliance with environmental requirements, including the Construction General Permit, at the ____________________________________ construction site.  The designee is authorized to sign any reports, stormwater pollution prevention plans and all other documents required by the permit.

________________________________________ (name of person or position)

________________________________________ (company)

________________________________________ (address)

________________________________________ (city, state, zip)

________________________________________ (phone)

By signing this authorization, I confirm that I meet the requirements to make such a designation as set forth in ____________________________________ (Reference State Permit), and that the designee above meets the definition of a “duly authorized representative” as set forth in ____________________________________ (Reference State Permit).

I certify under penalty of law that this document and all attachments were prepared under my direction or supervision in accordance with a system designed to assure that qualified personnel properly gathered and evaluated the information submitted.  Based on my inquiry of the person or persons who manage the system, or those persons directly responsible for gathering the information, the information submitted is, to the best of my knowledge and belief, true, accurate, and complete.  I am aware that there are significant penalties for submitting false information, including the possibility of fine and imprisonment for knowing violations.

Name:

Company:

Title:

Signature:

Date:

Appendix L –Standards and Specifications for Selected BMP’s

Appendix M –Standards and Specifications for Selected BMP’s