Hansen and Associates, Inc.

Consulting Engineers & Land Surveyors

April 2, 2014

Rochelle Pfeaster

Weber County Engineering

rpfeaster@co.weber.ut.us

Re: Bitton Subdivision

Dear Rochelle,

Transmitted herewith is our response to your review on the above referenced project:

- Spot shots and/or labeled contours must be submitted for review. Contours have been added.

- The proposed subdivision will need to have curb, gutter and sidewalk as per the county commission. As a bare minimum there will need to be a deferral on the curb, gutter and sidewalk, which has been signed by the developer prior to final approval. The developer will be requesting a deferral.

- The ditch in the front of the property will need to be piped with 18" concrete. If the ditch carries irrigation water, the irrigation company will need to approve the pipe size. If the curb, gutter and sidewalk are deferred, then the grade will need to be brought up to a foot below the edge of asphalt.  We are showing 18" dia. RCP to be placed in the existing ditch that run east - west through the property and across the front of the property.  The developer is submitting the plans to the Irrigation Co. for approval.

- A note will need to be added to the plat stating: "Due to the topography and the location of this subdivision all owners will accept responsibility for any storm water runoff from the road adjacent to this property until curb and gutter is installed." Added to Plat.

- Please show the existing ditches on the plat. There will need to be an easement given for the existing ditches in the subdivision. Done.

- It looks like there is an existing ROW running along a portion of this subdivision but not the full width, therefore dedication of the road will be required. Please show the existing property lines and the proposed dedication correctly. Done.

- An excavation permit is required for all work done within the existing right-of-way, including but not limited to piping of the existing ditch.  Will be done by the developer.

- All improvements need to be either installed or escrowed for prior to recording of the subdivision.  Will be done by the developer.

- The name and contact information of the developer must be on the plat. Done.

I trust this is satisfactory and meets your needs. If you have any questions or need more information, please let me  know.

Respectfully;

Hansen and Associates, Inc.

K. Greg Hansen, Pres. P.L.S.

Job No. 13-2-212