# Hansen and Associates, Inc.

# Consulting Engineers & Land Surveyors

August 22, 2023

Steve Burton, Weber County Planning

Tucker Weight, Weber County Engineering

Re:  Silverline Industrial Park Subdivision - response comments

Steve and Tucker,

This letter is for explanatory response comments for the County's latest review of the Silverline Industrial Park Subdivision.

(1)  The Remainder Parcel has been incorporated into Lot 2.  (Access easement to Remainder Parcel no longer pertinent).

(2)  I appreciate your explanation of the County's future plans for 9350 West.  The updated plat shows the depiction of an 80-foot wide 'Potential Future Roadway' which aligns with the centerline of 9350 West.  It's not an actual dedication at this time but shows an intended route of possible/likely public acquisition.  (Note: The straight 'tangent' section is 200 feet, the curve radii are 1000 feet).

(3)  Lot 1 is served by the access across lot 2, with verbiage placed in the Owner's Dedication.  The Lot 1 frontage is declared as a No Access Line.  Hopefully these actions will alleviate a need for frontage improvements. If 900 South road improvements are deemed necessary, the desire is that they be deferred, until perhaps in concert with development to the north.  Tie distance provided for easement across Lot 2.

(4)  900 South Street has an existing 33-foot south half street public road.  Additional road right-of-way was dedicated to Weber County per deed 2791028 (note:  15.57' dedication on one side and 19.66' dedication on the other side).  This plat offers a road dedication to the County to the fulfillment of a 60-foot south side dedication.

(5)  Monuments updated to reflect Weber County.

(6)  Addressing:  Lot 2 has an existing address of 9501 West - it would be a significant hassle to change - request to keep that address and have a new address for Lot 1.

Respectfully,

HANSEN & ASSOCIATES, Inc.

Jim Flint, PE / PLS